## Slide 1
Performance Evaluation of LoRa Networks
in a Smart City Scenario
Review by Tugrul Yatagan
yatagan@itu.edu.tr
Davide Magrin , Marco Centenaro and Lorenzo Vangelista
http://dx.doi.org/10.3390/s16091466

## Slide 2
Introduction
LoRa Technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
OUTLINE

## Slide 3
Introduction
LoRa
  Star topology
  Long range transmission in the License-free sub-GHz frequency
  Higher receiver sensitivity (PHY)
  These technologies trade data rate for coverage (data rate vs coverage)
Paper
  A new ns-3 module to study the performance of a LoRa-based IoT network in a typical urban scenario
  Results show that a LoRa network can scale well, achieving packet success rates above 95% in presence of a number of end devices in the order of 104
  LoRa networks that consider a number of end devices which are deployed in a realistic urban propagation scenario
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 4
LoRa technology
The LoRa Modulation
  LoRa is a proprietary PHY modulation designed and patented by Semtech Corporation
  Spreading Factor (SF), which can take values 7,8,9,10,11,12.
  The higher the SF is, the longer in time the packet and the more reliable its reception will be
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 5
LoRa technology
LoRaWAN
  LoRaWAN is open and described by the LoRa Alliance.
  Three main roles;
    The end device (or end node), that generates UL and/or receives downlink (DL) traffic.
    Gateways, which are devices that collect/send the packets coming from/sent to the end devices and forward/receive them to/from.
    The Network Server (NS), which plays the role of central coordinator and controller of the LoRa network.
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 6
LoRa technology
Frequency Bands and European Regulations
  LoRaWANs operate on the Industrial, Scientific, and Medical (ISM) frequency bands
    902 - 928 MHz band in the US and in the 863 - 870 MHz band in Europe
  Radios are required to adopt either a Listen-Before-Talk (LBT) policy or a duty cycled transmission to limit the rate.
  Three different categories of ISM sub-bands
    g1 line with maximum 36 seconds per hour Time on Air (ToA), 1% duty cycle to be shared between all sub-channels in each sub-band
    g1.2 with maximum 3.6 seconds per hour ToA, 0.1% duty cycle
    g1.3 with maximum 360 seconds per hour ToA, 10% duty cycle
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 7
Link-level Assumptions
System-level simulations are based on two models
  The link measurement model, used to abstract the effects of propagation on signal strength, fading and similar effects.
  The link performance model, which determines the probability of correctly receiving a packet at reduced complexity, the amount of interferers and other system-level effects
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 8
Link-level Assumptions
Link Measurement Model
  Given a transmitter-receiver pair, the link measurement model aims at estimating the strength of the signal at the receiver side.
  Receiver antenna gain with Gtx and Grc, respectively, and the transmit power with Ptx, L is the path loss. Then, the received power is expressed as;
  LdB consists of two contributions: the propagation loss, which depends on the distance between transmitter and receiver, and the building penetration loss, due to the wall attenuation.
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 9
Link-level Assumptions
Link Measurement Model
  The most common correlation model is a decaying exponential of distance.
  The distance between end nodes i and j with di,j , the shadowing correlation is;
  Assuming a shadowing decorrelation distance d0 = 110 m
  Regular grid in which each square has a side length of d0 (decorrelation distance) and draw an independent Gaussian random variable at each vertex of the grid.
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 10
Link-level Assumptions
Link Performance Model
  Abstracting the real implementation of the physical layer transmission chain and at making interference computations more manageable.
  Model of the gateway receiver and a pair of look-up tables that are used to model the aspects of sensitivity and interference.
  Si the sensitivity of the gateway receiver for SF = i.
  Increase of SF yields a better sensitivity.
  Any received packet with SF = i whose power is below the threshold Si cannot be detected by the gateway.
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 11
Link-level Assumptions
Link Performance Model
  Paper assume that interference only comes from other LoRa transmissions
  Different SFs to model whether a packet survives interference from other LoRa transmissions or not.
  (relative) Signal-to-Interference-plus-Noise-Ratio (SINR) threshold matrix;
  SINR margin (in dB units) that a packet sent with SF = i must have in order to be decoded if the interfering packet has SF = j.
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 12
System-level Assumptions
This paper explicitly refer to a LoRa Class A network, where transmissions are always initiated by the end devices
Every end device is assigned a random initial reporting delay (T seconds)
No DL transmissions, messages from the gateways to the end devices, are considered.
  DL transmissions is future work
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 13
System-level Assumptions
Spreading Factor Assignment
  At the beginning of the simulation, each device is assigned a SF as follows.
    Calculate the power level that each gateway would receive from the end device
    Pick the gateway with the highest received power and set the SF based on that value
    Assign the end device the lowest SF that would still be above the gateway sensitivity,
      Since we are interested, in general, in minimizing the ToA
    Note that, due to the shadowing and the presence of buildings, the closest gateway to a device may not always be the one that receives the highest power
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion

## Slide 14
Performance Evaluation
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Several tests were conducted in order to estimate throughput, packet error probability, and gateway coverage.
Throughput S as a function of the offered traffic G
A single central gateway and N end devices, uniformly distributed in a circular space around it of radius r = 7500 m (7500 is the maximum distance at which the gateway and an end device using SF = 12 are able to communicate)
For the throughput computation, the device i = 1, . . ,N generates every Ti seconds a packet which occupies the channel for tp,i seconds in order to be transmitted. Network offered traffic;
Given value of G, throughput S;
The probability of success of a given packet Psucc is the ratio between the number of successfully received packets and the total number of sent packets

## Slide 15
Performance Evaluation
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Throughput Performance (SF)

## Slide 16
Performance Evaluation
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Throughput Performance (Duty Cycle)

## Slide 17
Performance Evaluation
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Success Probability Performance
  The trend appears to be linear with the number of devices in the network, with a success probability around 97% for a network with 104 end devices

## Slide 18
Performance Evaluation
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Gateway Coverage Assessment
  In order to achieve a reliability above 90%, we should deploy gateways in such a way that every gateway covers 6 km2 or, equivalently, a radius of 1200 m around it.

## Slide 19
Conclusion
Introduction
LoRa technology
Link-level Assumptions
System-level Assumptions
Performance Evaluation
Conclusion
Simulation results show that;
  The LoRaWAN access scheme provides a higher throughput with respect to a basic ALOHA scheme, thanks to the partial orthogonality between its spreading factors.
  The LoRaWAN architecture can scale well, mainly due to the fact that an increase in the number of gateways enhances the coverage and reliability of the uplink as well.
  A network featuring multiple gateways and a realistic traffic model resulted in a packet success rate above 95% for a gateway serving approximately 15000 end devices.
Future work;
  The effectiveness of different ADR (Adaptive Data Rate) schemes
  Investigate optimal gateway placement
  Frequency planning and co-existence with other networks working in the unlicensed spectrum

## Slide 20
Thank you for your time.
Any questions?