## Slide 1
Low Power Wide Area Networks: An Overview
Review by
U. Raza, P. Kulkarni and M. Sooriyabandara, "Low Power Wide Area Networks: An Overview" in IEEE Communications Surveys & Tutorials, vol. 19, no. 2, pp. 855-873, second quarter 2017 doi: 10.1109/COMST.2017.2652320
Tuğrul Yatağan
yatagan@itu.edu.tr
504161551
Sinan Atan
atan@itu.edu.tr
504162306

## Slide 2
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Outline

## Slide 3
Introduction
Number of connected M2M devices and consumer electronics will surpass the number of human subscribers by 2020 [1]
IoT industry is expected to generate a revenue of 4.3 trillion dollars by 2024 [2]
How to provide connectivity for low power devices distributed over large geographical areas?
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
1. Image Source: https://www.slideshare.net/PeterREgli/lpwan
Figure 1: Wireless technologies with respect to range and data rate1
LPWAN fills the technology gap between;
  Short range wireless technologies (ZigBee, Bluetooth, Wi-Fi)
    Very costly to deploy massive/dense # of devices
  Cellular (2G, 3G, 4G)
    Optimized for voice and data
    Complex and expensive
    High power consumption
RANGE
DATA RATE
LPWA application areas;
  Smart city
  Personal IoT
  Smart grid metering
  Agriculture
  Industrial assets monitoring
  Home automation
  Logistics
  Wildfire monitoring
Notes: The range of short range wireless technologies is limited to a few hundred meters at best. Dense deployment needed. Multihop, mesh

## Slide 4
Introduction
Low Power Wide Area (LPWA) networks;
Low power (ten years and beyond)
Long range (a few to tens of kilometers)
Low cost
High scalability
Low data rate (in orders of tens of kilobits per seconds)
High latency (in orders of seconds or minutes)
LPWAN applicable applications;
  Delay tolerant
  Low data rates
  Low power consumption
Several competing standards development organizations;
1. Image Source: https://www.slideshare.net/PeterREgli/lpwan
  ETSI
  3GPP
  IEEE
  IETF
Several competing alliances;
  LoRaTM Alliance
  Weightless SIG
  DASH 7 Alliance
Figure 2: Wireless technologies with respect to various properties1
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Notes: LPWAN is not suitable for many industrial IoT, vehicle to vehicle (V2V), and vehicle to infrastructure (V2I) applications
European Telecommunications Standard Institute
Third Generation Partnership Project
Institute of Electrical and Electronics Engineers
Internet Engineering Task Force

## Slide 5
Design Goals and Techniques
Key objectives of LPWAN technologies; long range + low power + low cost
Long range
  Sub-GHz band
    Lower frequency signals experience less attenuation and multipath fading
  Special modulation techniques
    Designed to achieve a link budget of 150 ± 10 dB that enables a range of a few km and tens of km
    Two classes of main modulation techniques;
      Narrowband; encoding the signal in low bandwidth (usually less than 25kHz)
        Reduce noise, decrease data rate
      Spread spectrum; spread signal over a wider frequency band but with the same power density
        Resilient to interference, harder to decode
Low cost
  Cost of hardware should below $10 and connectivity subscription per unit should low as $1
  Reduction in hardware complexity
  Minimum infrastructure
  Using license-free or already owned licensed bands
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Notes: Key objectives are conflicting each other.
Narrowband share the overall spectrum very efficiently between multiple links. NB-IoT, WEIGHTLESS-P and SIgFox (100Hz)
Compared to the cellular and the short range wireless technologies
dense and therefore an expensive deployment

## Slide 6
Design Goals and Techniques
Ultra low power operation
  Simple topology
    No mesh, direct connection from end devices to base stations
  Duty cycling
    End devices to turn off their transceivers when not required
  Lightweight medium access control
    Widely used MAC protocols (cellular, WLAN) are too complex. Mostly ALOHA is used
  Offloading complexity from end devices
    Simplify the design of end devices, move complexity to base stations and backend system
Scalability
  Diversity; channel, time, space, and hardware
  Densification
  Adaptive channel selection and data rate
Quality of service
  Limited or no QoS
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Notes: Backend system adapts communication parameters (such as data rate/ modulation parameters)
not to waste precious energy in busy-listening to other devices
No CSMA/CA

## Slide 7
Proprietary Technologies
Sigfox
  Patented, proprietary base stations and proprietary network operator
  Ultra-low power consumption and inexpensive antenna design
  Maximum uplink throughput of only 100 bps!
  140 12-byte uplink and 4 8-bytes downlink messages limit per day!
  Single message is transmitted multiple times (3 by default) for reliability, no acknowledgments
LoRa
  Modulates the signals in Sub-GHz ISM band using a proprietary spread spectrum technique CSS
  Resilient to interference and noise
  Multiple spreading factors (between 7-12) to decide the tradeoff between range and data rate
  Data rate ranges from 300 bps to 37.5 kbps depending on spreading factor
  The messages transmitted by the end devices are received by all the base stations in the range -> localization
  LoRaWAN is open standard MAC layer protocol for LoRa physical layer
    Battery Powered – Class A
    Low Latency – Class B
    No Latency – Class C
1. Image Source: https://i1.wp.com/www.zerynth.com/wp-content/uploads/2017/05/lorawan-architecture.jpg?resize=1024%2C561&ssl=1
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Figure 3: LoRa Topology1
Notes: Higher spreading factors delivers long range at an expense of lower data rates and vice versa

## Slide 8
Proprietary Technologies
Table 1: Technical specifications of proprietary LPWA technologies
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion

## Slide 9
Organizations for Standards
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion

## Slide 10
Developed Standards
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
LPWA Standards
IEEE
802.15.4k
802.15.4g
802.11: Long Range Low Power (LRLP)
ETSI
Low Throughput Networks (LTN)
3GPP
Enhanced MTC (eMTC)
Extended Coverage GSM (EC-GSM)
Narrowland IoT (NB-IoT)
IEFT
6LPWA/LP-WAN
Weightless-SIG
Weightless-W/N/P
LoRa Alliance
LoRaWAN
Dash7 Alliance
DASH7
Why Standards:
Unified end user experience
  GSM and IS-95 in 2G
Reduced project risks
Enable easier and cheaper integrity
To achieve inter-vendor operability
  Reducing investment costs
Enable in-house developments
  Which is very valuable for IoT environment
Objectives of SDOs and SIGs are diverse.
In the long run, it is expected to enable coexistence of competing Technologies with the adaptation of these standards.
Figure 4: LPWA standards and their developing organizations.

## Slide 11
Comparison of Standards
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Table 2: Technical specifications of various LPWA standards (?=Not known)
Notes: DSSS Direct Sequence Spread Spectrum

## Slide 12
Challenges and Open Research Directions
LPWA striving hard to deliver innovative solutions securing carrier grade performance in case of:
Scaling networks to massive number of devices
Interference control and mitigation
High data rate modulation techniques
Interoperability between different LPWA technologies
Localization
Link optimizations and adaptability
Testbeds and tools
Authentication, security & privacy
Mobility & roaming
Support for service level agreements
Co-Existence of LPWA technologies with other wireless networks
Support for data analytics
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion

## Slide 13
Challenges and Open Research Directions
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
Table 3: Business considerations for various LPWA technologies (?=Not known)

## Slide 14
Conclusion
Introduction
Design Goals and Techniques
Proprietary Technologies
Standards
Challenges and Open Research Directions
Conclusion
In this paper:
Low Power Wide Area Network Technologies and Standards surveyed.
Design criterias and Open Research Areas on this topic briefly described.
Business considerations are given.
LPWA applications in different sectors are sampled.
It is observed that:
Key features of a LPWA technology are;
  Low power consumption
  Wide area coverage
  Inexpensive wireless connectivity
Each technology driven by different SDOs/SIGs have pros and cons
There exists several common vulnerabilities in LPWA motivating researchers
Existing Technologies in MAC & PHY layers does not fulfill LPWA design principles
Many Technologies with different design principles causing questionmarks about interoperability
3GPPs NB-IOT still in draft state, it would provide a main standard for all organizations to follow